## Slide 1: Balloon Aerosols Instruments for the Validation of EarthCare (BAIVEC)
Jean-Baptiste RENARD, LPC2E, Orléans, France
Albert HERTZOG, LMD, Palaiseau, France
Gwenaël BERTHET, Fabrice JEGOU, LPC2E-CNRS, Orléans, France
François RAVETTA, LATMOS, Paris,France
Hélène CHEPFER, Artem FEOFILOV, Vincent NOEL, LMD, Palaiseau, France

## Slide 2
Validation of EarthCare aerosol measurements, during good temporal and spatial coincidences with balloon-borne measurements
Already successful strategy in the past for the validation of chemistry instruments onboard Envisat, with the launch of “big” balloons by the CNES at different latitudes
UV-visible spectrometer SALOMON

## Slide 3
Example of validation of the O3 and NO2 GOMOS measurements with the balloon-borne UV-visible spectrometer SALOMON, from south-west of France, colocation of about 100 km and 1 hour
Validation exercise has been useful to improve the GOMOS algorithm
NO2
O3

## Slide 4
We propose here an easy-to -conduct strategy:
Use of the LOAC aerosol counter under « Light Dilatable Balloons » (weather balloons)
Coincidence opportunity with the aerosol measurements onboard the long-duration balloons of the Strateole project

## Slide 5
Light Optical Aerosols counter (LOAC)
Size distribution for 19 size classes in the 0.2 – 50 mm range
Measurements at 2 scattering angles (field of view of few degrees)
~12°, insensitive to the refractive index of the particles (mainly diffraction)
=> accurate size determination and counting
~60°, strongly sensitive to the refractive index of the particles
=> indication of the typology of the particles

## Slide 6
Indication of typology of the aerosols:
The 60° measurements are sensitive to the refractive index of the aerosols
More absorbing are the particles, lower is the scattered flux;
the measurements at 60° are often lower than the measurements at 12°
The ratio of the 2 size distributions varies with the light-absorbing properties of the particles (“speciation index”)
Comparison of the measured “speciation index” with laboratory measurements of pure particles, to provide reference speciation zones

## Slide 7
Since 2013, about 150 LOAC launches from different latitudes, even in difficult weather conditions !
Measurements from ground to the middle stratosphere

## Slide 8
Conversion of the LOAC counting to extinctions, using the estimated typology for the choice of the refractive index
Example of comparison of LOAC with Caliop/Calispo during dust events above the Mediterranean sea, with same typology identification by the 2 instruments, during a good coincidence (< 200 km and < 2 hours)
LOAC typology identification

## Slide 9
Another approach: Statistical comparison between 23 LOAC flight above the South-West of France in 2014-2015 (background conditions only) and Caliop extinctions in same location and conditions
Mean values and dispersion of the measurements

## Slide 10
BAIVEC project
Preparation
Several LOAC flights per year in good coincidence with Caliop from South-West of France, performed by CNES (from summer 2018)
Campaign
- ~15 flights per year in South-West of France (CNES) in good coincidence, and flights under alert in specific conditions like dust event, pollution
- Opportunity flights at other latitudes (Ile de la Réunion, Iceland, …) in the frame of the other LOAC scientific campaigns
- Comparison with EarthCare extinctions profiles

## Slide 11
Also opportunity coincidences with the measurements onboard the Strateole balloons (France – USA project) launched by CNES
Long duration balloon flights of 3 months in the tropical region, 2020-2023 (tests campaign in 2019, then 2 campaigns), altitude of 16-20 km, thousands of coincidences expected
  LOAC
  Lidar BeCOOL
  Backscatter sounding
Validation of EarthCare backscatter, scattering ratio and extinction profiles

## Slide 12
LOAC instrument fully operational and use in routine since 5 years, data from « Light Dilatable Balloons » available just after the flights
2 to 4 reports provided per year
Strateole data available at the end of each campaigns
Reports after each Strateole campaign